Alliance Drywall Services

(816) 985-9280

I developed this list after building several new homes.  I never planned to be a professional builder because that competes with my customers.  Therefore, I’m not a builder.  But I do believe that if you have made the decision to build your own home then my roll as a subcontractor is to help you through the process.

You can apply this list to any home construction process just by skipping the tasks that do not apply.

I appreciate the feedback from past customers as to what needs to be changed on this list.

Mark

Master Schedule – New Home Construction                    7-13-06

Begin Construction Project Book

Lot Search

Check restrictions

Check economy

Location of utilities

Obvious content and foundation needs (any fill or rock?)

How deep in the sewer line, especially in older sub-divisions

Determine Size of Home

Determine if Septic Required

Test Soil

Get design if required

Obtain installation bid

Obtain Land Financing

Purchase Lot

Septic approved before lot purchase

Get septic permit and stake off lines

Check for set backs and other legal issues

Consider lot purchase at same time as permit in case there are issues

Meet the neighbors because they will be upset later during construction

Evaluate Floor Plans / Make Design Changes

Obtain Bids

Lumber company to engineer floor joist

Cut Costs as Required

Obtain End Mortgage Financing

Apply For Construction Loan

Go by the post office or city for address assignment

Can use the lot number for short-term needs

While at post office find out about box specifications/mounting heights

Establish Project Checking Account

Obtain Building Permit/Minimum Occupancy Requirements

Need plumbing, hvac, electrical subs listed

Need plot plan

Need total costs

Obtain Builder’s Risk and Liability Insurance

Call Before You Dig

Find Utility Services in order to Sleeve Foundation Walls as Needed

Stake Lot

Post Permit and Trespass Signs on Lot

Install Septic as Required

May need rock for lines

Leave lines open for inspection

Hookup electric to pump if required

Call for pump hookup

Call for inspection

Backfill septic and rope off area so no one drives on lateral field

Plant grass Seed if not sodding

Arrange for Portable Toilet

Order Temp. Power

Install base

Call for inspection

Have utility hookup power

Order Windows (2 weeks lead time, 3 if custom)

Order Trusses if Required

Does the order include boom time?

Excavate Foundation

Pour Foundation

Have foundation company calls for own inspections

Order footer lumber

Pour footer

Pour foundation walls

Pour retaining walls as required

Gravel drive

Sleeve walls for utilities if needed

Use Engineered Floor in Garage if Back-filled

Will need a column in center (ranch style garages)

Knock-off Foundation Ties (leave some for shelving or room under porch)

Mark sleeves that will be under ground (such as sewer)

Water Proof Walls

Coordinate with striping of foundation walls

One load ½ clean rock

Make sure sub knows the grade on side of house; the black material is hard to paint if you get it above the grade line.

Termite and Insect Spray Walls

Backfill Drain Tiles (1/2 or ¾ clean rock 20 tons does 1000 sq.ft.)

Plumbing Ground Rough

Call for inspection

May need gravel

Sewer and Water Hookup to Main

Mark water meter with board to prevent cover up

Will need gravel for sewer

Pour Basement Floor (25-40 degrees min.)

Supply anchor bolts for any walkout walls to be constructed

Backfill House

Order Gas Lines

Set I Beam (2 day lead time)

Order Rough-in Lumber

Order Delivery of Windows

Order Vanity Tops and Cabinets

Rough-in House

Install Roof Trusses

Evaluate Boom truck access

Order 1st Dumpster

Shingle Roof

Pour Garage Floor Concrete

Mechanical Rough-In (call when roof sheeting going on)

Any pre-sheetrock needed for tight walls behind furnace and other?

Plumbing Rough-in

Box in heat ducts

Insulate Behind Showers (no plastic)

Schedule rain day

Cover floor drains to keep foreign items out

Order Gas Meter – Winter Only

Electrical Rough-in

Stereo wires

Verify cable/phone

Watch for cabinet locations

Install Fireplace

Rough-in Crew Back for Drops Around HVAC ect..

Rough-in Cleanup

Fire Caulk

Window Insulation and Caulking

Call for Rough-In Inspection

Pour Drive, Walks and Patio, Dog Kennels

Front sidewalk if required

Build Deck

Could Effect Siding Contractor

Order Garage Doors

Call for Electrical Service

Call for Water Meter

Call For Gas Service if Not Winter

Insulation Walls and Batts for Ceiling, Caulking as Required

If using siding make sure the soffits are in for winter work as you will

Want to blow the attic early.

USDA inspection (502 direct and blended) if Applicable

Make Final Color Selections

Order Siding

Schedule delivery out of way of sheetrock

Install Siding if Sheetrock Delayed

Paint foundation before siding/guttering

Sheetrock

Schedule rain day

Cleanup

Final Grade

Install Rock or Brick as Required

Install Siding if Sheetrock Not Delayed

Need soffit for insulation

Install Garage Doors

Have weather stripping installed if no siding

Insulate Attic

Schedule Trim Delivery

Include front posts, rails, base shoe

Paint Ceilings as Required

Install Hardwood Floors

Install Cabinets

Order Appliances

Cleanup - Vacuum

Trim

Set front posts, stair handrails

Trim Cleanup

Paint and Stain

Paint foundation before siding/guttering

Make sure shutters are painted

Make sure base shoe is stained

Make sure nails pounded in on siding

Guttering

Electrical Finish

HVAC Finish

Call cable and phone as required

Underlayment Installation

Sand hardwood 1st coat

Hardwood 2nd coat

Cleanup for Carpet/Vinyl - Vacuum

Carpet and Vinyl

Install carpet protector

Base Shoe

Deliver Vanity Tops and Appliances

Call electrical company back to install

Plumbing Finish

Final Grade if Not Done

Landscape and Sod or Seed

Detail House

Shower and mirror installation

Hardwood floor 3rd coat

Misc. tough-up

Install hardware

Hang Doors

Mailbox

Shutters

House numbers

Base shoe

Final Cleanup

Schedule rain day

Final Inspection

Appraiser

Walk Through with Owner

Closing